## Slide 1
Ansys Fluent Simulation Report

## Slide 2: Header
Analyst | ShubhamR
Date | 2/8/2026 11:17 AM
Table of contents

## Slide 3: Table of Contents
System Information
Geometry and Mesh
  Mesh Size
  Mesh Quality
  Orthogonal Quality
Simulation Setup
  Physics
    Models
    Material Properties
    Cell Zone Conditions
    Boundary Conditions
    Reference Values
  Solver Settings
Run Information
Solution Status
Named Expressions
Report Definitions
Plots
  Residuals
  Report Plots
Contours
Vectors
Pathlines

## Slide 4: System Information
Application | Fluent
Settings | 2d, double precision, density-based explicit, Spalart-Allmaras
Version | 25.2.0-10204
Source Revision | 5eecd5d865
Build Time | Jun 16 2025 10:44:41 EDT
CPU | AMD Ryzen 7 6800H with Radeon Graphics
OS | Windows
Table of contents
System Information

## Slide 5
Table of contents
Geometry and Mesh
Geometry and Mesh

## Slide 6: Mesh Size
Cells | Faces | Nodes
39 | 140 | 0
118 | 415 | 0
351 | 1192 | 0
1023 | 3254 | 0
3288 | 9800 | 0
22914 | 35063 | 12153
Table of contents
Geometry and Mesh / Mesh Size

## Slide 7: Mesh Quality
Name | Type | Min Orthogonal Quality | Max Aspect Ratio
fluid | Tri Cell | 0.65988415 | 3.7977613
solid | Tri Cell | 0.65917937 | 3.7967206
Table of contents
Geometry and Mesh / Mesh Quality

## Slide 8: Orthogonal Quality
Table of contents
Geometry and Mesh / Orthogonal Quality

## Slide 9
Table of contents
Simulation Setup
Simulation Setup

## Slide 10
Table of contents
Simulation Setup / Physics
Physics

## Slide 11: Models
Model | Settings
Space | 2D
Time | Steady
Viscous | Spalart-Allmaras turbulence model
Production Option | Vorticity
Heat Transfer | Enabled
Table of contents
Simulation Setup / Physics / Models

## Slide 12: Material Properties
- Fluid | 
- air | 
Density | ideal gas
Cp (Specific Heat) | 1006.43 J/(kg K)
Thermal Conductivity | 0.0242 W/(m K)
Viscosity | 1.7894e-05 kg/(m s)
Molecular Weight | 28.966 kg/kmol
- Solid | 
- aluminum | 
Density | 2719 kg/m^3
Cp (Specific Heat) | 871 J/(kg K)
Thermal Conductivity | 202.4 W/(m K)
Table of contents
Simulation Setup / Physics / Material Properties

## Slide 13: Cell Zone Conditions
- Fluid | 
- fluid | 
Material Name | air
Specify source terms? | no
Specify fixed values? | no
Frame Motion? | no
Laminar zone? | no
Porous zone? | no
- Solid | 
- solid | 
Material Name | aluminum
Specify source terms? | no
Frame Motion? | no
Table of contents
Simulation Setup / Physics / Cell Zone Conditions (1 of 2)

## Slide 14: Cell Zone Conditions
Solid Motion? | no
Table of contents
Simulation Setup / Physics / Cell Zone Conditions (2 of 2)

## Slide 15: Boundary Conditions
- Inlet | 
- inlet | 
Gauge Pressure [Pa] | 101325
Mach Number | 1.1
Temperature [K] | 300
Component of Flow Direction (x,y) | (1, 0)
Turbulence Specification Method | Turbulent Viscosity Ratio
Turbulent Viscosity Ratio | 10
- outlet | 
Gauge Pressure [Pa] | 101325
Mach Number | 1.1
Temperature [K] | 300
Component of Flow Direction (x,y) | (1, 0)
Table of contents
Simulation Setup / Physics / Boundary Conditions (1 of 4)

## Slide 16: Boundary Conditions
Turbulence Specification Method | Turbulent Viscosity Ratio
Turbulent Viscosity Ratio | 10
- Wall | 
- soild_wall | 
Wall Thickness [m] | 0
Heat Generation Rate [W/m^3] | 0
Material Name | aluminum
Thermal BC Type | Heat Flux
Heat Flux [W/m^2] | 0
Convective Augmentation Factor | 1
- soild_wall:001 | 
Wall Thickness [m] | 0
Heat Generation Rate [W/m^3] | 0
Table of contents
Simulation Setup / Physics / Boundary Conditions (2 of 4)

## Slide 17: Boundary Conditions
Material Name | aluminum
Thermal BC Type | Coupled
Wall Motion | Stationary Wall
Shear Boundary Condition | No Slip
Wall Surface Roughness | Standard
Wall Roughness Height [m] | 0
Wall Roughness Constant | 0.5
Convective Augmentation Factor | 1
- soild_wall:001-shadow | 
Wall Thickness [m] | 0
Heat Generation Rate [W/m^3] | 0
Material Name | aluminum
Thermal BC Type | Coupled
Table of contents
Simulation Setup / Physics / Boundary Conditions (3 of 4)

## Slide 18: Boundary Conditions
Convective Augmentation Factor | 1
Table of contents
Simulation Setup / Physics / Boundary Conditions (4 of 4)

## Slide 19: Reference Values
Area | 1 m^2
Density | 1.225 kg/m^3
Depth | 1 m
Enthalpy | 0 J/kg
Length | 1 m
Pressure | 0 Pa
Temperature | 288.16 K
Velocity | 1 m/s
Viscosity | 1.7894e-05 kg/(m s)
Ratio of Specific Heats | 1.4
Yplus for Heat Tran. Coef. | 300
Reference Zone | fluid
Table of contents
Simulation Setup / Physics / Reference Values

## Slide 20: Solver Settings
- Equations | 
Flow | True
Modified Turbulent Viscosity | True
- Numerics | 
Absolute Velocity Formulation | True
- Under-Relaxation Factors | 
Modified Turbulent Viscosity | 0.8
Turbulent Viscosity | 1
Solid | 1
- Discretization Scheme | 
Flow | Second Order Upwind
Modified Turbulent Viscosity | Second Order Upwind
- Time Marching | 
Table of contents
Simulation Setup / Solver Settings (1 of 3)

## Slide 21: Solver Settings
Solver | Explicit
Courant Number | 0.05
Residual Smoothing Iterations | 0 (disabled)
Residual Smoothing Factor | 0.5
- Multigrid Solver | 
Coarse Grid Levels | 5
Fine Grid Iterations | 1
Final Iterations | 0
Time Step Reduction | 0.9
Correction Reduction | 0.6
Species Correction Reduction | 1
Correction Smoothing Factor | 0.5
- Multi-Stage Scheme | 
Table of contents
Simulation Setup / Solver Settings (2 of 3)

## Slide 22: Solver Settings
1 | 0.2075
2 | 0.5915
3 | 1
- Solution Limits | 
Minimum Absolute Pressure [Pa] | 1
Maximum Absolute Pressure [Pa] | 5e+10
Minimum Static Temperature [K] | 1
Maximum Static Temperature [K] | 5000
Maximum Turb. Viscosity Ratio | 100000
Table of contents
Simulation Setup / Solver Settings (3 of 3)

## Slide 23: Run Information
Number of Machines | 1
Number of Cores | 2
Case Read | 7.168 seconds
Iteration | 153.359 seconds
AMG | 1.133 seconds
Virtual Current Memory | 1.0861 GB
Virtual Peak Memory | 1.1983 GB
Memory Per M Cell | 19.0502
Table of contents
Run Information

## Slide 24: Solution Status Iterations: 4585
 | Value | Absolute Criteria | Convergence Status
continuity | 0.0009998756 | 0.001 | Converged
x-velocity | 0.0001775964 | 0.001 | Converged
y-velocity | 0.0005544375 | 0.001 | Converged
energy | 0.0008708995 | 0.001 | Converged
nut | 0.0002517476 | 0.001 | Converged
Table of contents
Solution Status

## Slide 25: Named Expressions
Expression | Definition | Value | Unit | Used In | Description
expr1 | Maximum(MachNumber, ['fluid']) | 1.9877734 | [] | report-def-0-sa (Report Definition) | 
Table of contents
Named Expressions

## Slide 26: Report Definitions
report-def-0-sa | 1.987773 | 
Table of contents
Report Definitions

## Slide 27
Table of contents
Plots
Plots

## Slide 28: Residuals
Chart: Residuals
Table of contents
Plots / Residuals

## Slide 29
Table of contents
Plots / Report Plots
Report Plots

## Slide 30: report-def-0-rplot
Chart: report-def-0-rplot
Table of contents
Plots / Report Plots / report-def-0-rplot

## Slide 31
Table of contents
Contours
Contours

## Slide 32: contour-3-x_velocity
Table of contents
Contours / contour-3-x_velocity

## Slide 33: contour-2-total_temperature
Table of contents
Contours / contour-2-total_temperature

## Slide 34: contour-1-static_pressure
Table of contents
Contours / contour-1-static_pressure

## Slide 35
Table of contents
Vectors
Vectors

## Slide 36: vector-1
Table of contents
Vectors / vector-1

## Slide 37
Table of contents
Pathlines
Pathlines

## Slide 38: pathlines-2-mach_number
Table of contents
Pathlines / pathlines-2-mach_number

## Slide 39: pathlines-1-density
Table of contents
Pathlines / pathlines-1-density