## Slide 1
Ansys Fluent Simulation Report

## Slide 2: Header
Analyst | ShubhamR
Date | 8/19/2026 10:57 PM
Table of contents

## Slide 3: Table of Contents
System Information
Geometry and Mesh
  Mesh Size
  Mesh Quality
  Orthogonal Quality
Simulation Setup
  Physics
    Models
    Material Properties
    Cell Zone Conditions
    Boundary Conditions
    Reference Values
  Solver Settings
Run Information
Solution Status
Plots
  Residuals
Mesh
Contours
Pathlines
Scenes

## Slide 4: System Information
Application | Fluent
Settings | 3d, double precision, pressure-based, SST k-omega
Version | 26.1.0-10262
Source Revision | b6f454dde8
Build Time | Feb 2 2026 16:34:25 EST
CPU | AMD Ryzen 7 6800H with Radeon Graphics
GPU | NVIDIA GeForce RTX 3050 Laptop GPU
OS | Windows
Table of contents
System Information

## Slide 5
Table of contents
Geometry and Mesh
Geometry and Mesh

## Slide 6: Mesh Size
Cells | Faces | Nodes
107676 | 241529 | 33214
Table of contents
Geometry and Mesh / Mesh Size

## Slide 7: Mesh Quality
Name | Type | Min Orthogonal Quality | Max Aspect Ratio
fluid | Mixed Cell | 0.22227342 | 14.697877
solid11 | Tet Cell | 0.12993988 | 20.319746
Table of contents
Geometry and Mesh / Mesh Quality

## Slide 8: Orthogonal Quality
Table of contents
Geometry and Mesh / Orthogonal Quality

## Slide 9
Table of contents
Simulation Setup
Simulation Setup

## Slide 10
Table of contents
Simulation Setup / Physics
Physics

## Slide 11: Models
Model | Settings
Space | 3D
Time | Steady
Viscous | SST k-omega turbulence model
Table of contents
Simulation Setup / Physics / Models

## Slide 12: Material Properties
- Fluid | 
- water-liquid | 
Density | 998.2 kg/m^3
Viscosity | 0.001003 kg/(m s)
- air | 
Density | 1.225 kg/m^3
Viscosity | 1.7894e-05 kg/(m s)
- Solid | 
- steel | 
Density | 8030 kg/m^3
- aluminum | 
Density | 2719 kg/m^3
Table of contents
Simulation Setup / Physics / Material Properties

## Slide 13: Cell Zone Conditions
- Fluid | 
- fluid | 
Material Name | water liquid
Specify source terms? | no
Specify fixed values? | no
Frame Motion? | no
Laminar zone? | no
Porous zone? | no
3D Fan Zone? | no
- Solid | 
- solid11 | 
Material Name | steel
Frame Motion? | no
Table of contents
Simulation Setup / Physics / Cell Zone Conditions (1 of 2)

## Slide 14: Cell Zone Conditions
Solid Motion? | no
Table of contents
Simulation Setup / Physics / Cell Zone Conditions (2 of 2)

## Slide 15: Boundary Conditions
- Inlet | 
- inlet | 
Velocity Specification Method | Magnitude, Normal to Boundary
Reference Frame | Absolute
Velocity Magnitude [m/s] | 10
Supersonic/Initial Gauge Pressure [Pa] | 0
Turbulence Specification Method | Intensity and Viscosity Ratio
Turbulent Intensity [%] | 5
Turbulent Viscosity Ratio | 10
- Outlet | 
- outlet | 
Backflow Reference Frame | Absolute
Gauge Pressure [Pa] | 0
Table of contents
Simulation Setup / Physics / Boundary Conditions (1 of 3)

## Slide 16: Boundary Conditions
Pressure Profile Multiplier | 1
Backflow Direction Specification Method | Normal to Boundary
Turbulence Specification Method | Intensity and Viscosity Ratio
Backflow Turbulent Intensity [%] | 5
Backflow Turbulent Viscosity Ratio | 10
Backflow Pressure Specification | Total Pressure
Build artificial walls to prevent reverse flow? | no
Radial Equilibrium Pressure Distribution (Unsupported) | no
Average Pressure Specification? | no
Specify targeted mass flow rate | no
- Wall | 
- fluid-solid11 | 
Wall Motion | Stationary Wall
Table of contents
Simulation Setup / Physics / Boundary Conditions (2 of 3)

## Slide 17: Boundary Conditions
Shear Boundary Condition | No Slip
Wall Surface Roughness | Standard
Wall Roughness Height [mm] | 0
Wall Roughness Constant | 0.5
surface:1 | wall
solid11:655 | wall
fluid-solid11-shadow | wall
Table of contents
Simulation Setup / Physics / Boundary Conditions (3 of 3)

## Slide 18: Reference Values
Area | 1 m^2
Density | 998.2 kg/m^3
Enthalpy | 0 J/kg
Length | 1 mm
Pressure | 0 Pa
Temperature | 288.16 K
Velocity | 10 m/s
Viscosity | 0.001003 kg/(m s)
Ratio of Specific Heats | 1.4
Yplus for Heat Tran. Coef. | 300
Reference Zone | fluid
Table of contents
Simulation Setup / Physics / Reference Values

## Slide 19: Solver Settings
- Equations | 
Flow | True
Turbulence | True
- Numerics | 
Absolute Velocity Formulation | True
- Under-Relaxation Factors | 
Pressure | 0.3
Density | 1
Body Forces | 1
Momentum | 0.7
Turbulent Kinetic Energy | 0.8
Specific Dissipation Rate | 0.8
Turbulent Viscosity | 1
Table of contents
Simulation Setup / Solver Settings (1 of 3)

## Slide 20: Solver Settings
- Pressure-Velocity Coupling | 
Type | SIMPLE
- Discretization Scheme | 
Pressure | Second Order
Momentum | Second Order Upwind
Turbulent Kinetic Energy | Second Order Upwind
Specific Dissipation Rate | Second Order Upwind
- Solution Limits | 
Minimum Absolute Pressure [Pa] | 1
Maximum Absolute Pressure [Pa] | 5e+10
Minimum Static Temperature [K] | 1
Maximum Static Temperature [K] | 5000
Minimum Turb. Kinetic Energy [m^2/s^2] | 1e-14
Table of contents
Simulation Setup / Solver Settings (2 of 3)

## Slide 21: Solver Settings
Minimum Spec. Dissipation Rate [s^-1] | 1e-20
Maximum Turb. Viscosity Ratio | 100000
Table of contents
Simulation Setup / Solver Settings (3 of 3)

## Slide 22: Run Information
Number of Machines | 1
Number of Cores | 4
Case Read | 22.757 seconds
Data Read | 0.387 seconds
Virtual Current Memory | 8.4766 GB
Virtual Peak Memory | 8.4956 GB
Memory Per M Cell | 72.5015
Table of contents
Run Information

## Slide 23: Solution Status Iterations: 2000
 | Value | Absolute Criteria | Convergence Status
continuity | 0.0004435178 | 0.001 | Converged
x-velocity | 0.00247927 | 0.001 | Not Converged
y-velocity | 0.001759697 | 0.001 | Not Converged
z-velocity | 0.001828777 | 0.001 | Not Converged
k | 0.001399828 | 0.001 | Not Converged
omega | 0.001396939 | 0.001 | Not Converged
Table of contents
Solution Status

## Slide 24
Table of contents
Plots
Plots

## Slide 25: Residuals
Chart: Residuals
Table of contents
Plots / Residuals

## Slide 26
Table of contents
Mesh
Mesh

## Slide 27: mesh-1
Table of contents
Mesh / mesh-1

## Slide 28
Table of contents
Contours
Contours

## Slide 29: contour-1
Table of contents
Contours / contour-1

## Slide 30
Table of contents
Pathlines
Pathlines

## Slide 31: pathlines-1
Table of contents
Pathlines / pathlines-1

## Slide 32
Table of contents
Scenes
Scenes

## Slide 33: scene-1
Table of contents
Scenes / scene-1