## Slide 1
Ansys Fluent Simulation Report

## Slide 2: Header
Analyst | ShubhamR
Date | 2/7/2026 08:45 PM
Table of contents

## Slide 3: Table of Contents
System Information
Geometry and Mesh
  Mesh Size
  Mesh Quality
  Orthogonal Quality
Simulation Setup
  Physics
    Models
    Material Properties
    Cell Zone Conditions
    Boundary Conditions
    Reference Values
  Solver Settings
Run Information
Solution Status
Report Definitions
Plots
  Residuals
Contours
Vectors
Pathlines

## Slide 4: System Information
Application | Fluent
Settings | 2d, double precision, pressure-based, dynamic mesh, Scale Adaptive Simulation, transient
Version | 25.2.0-10204
Source Revision | 5eecd5d865
Build Time | Jun 16 2025 10:44:41 EDT
CPU | AMD Ryzen 7 6800H with Radeon Graphics
OS | Windows
Table of contents
System Information

## Slide 5
Table of contents
Geometry and Mesh
Geometry and Mesh

## Slide 6: Mesh Size
Cells | Faces | Nodes
5840 | 8882 | 3043
Table of contents
Geometry and Mesh / Mesh Size

## Slide 7: Mesh Quality
Name | Type | Min Orthogonal Quality | Max Aspect Ratio
fluid | Tri Cell | 0.1127685 | 10.245138
solid | Tri Cell | 0.76980036 | 3.1622777
Table of contents
Geometry and Mesh / Mesh Quality

## Slide 8: Orthogonal Quality
Table of contents
Geometry and Mesh / Orthogonal Quality

## Slide 9
Table of contents
Simulation Setup
Simulation Setup

## Slide 10
Table of contents
Simulation Setup / Physics
Physics

## Slide 11: Models
Model | Settings
Space | 2D
Time | Unsteady, 1st-Order Implicit
Viscous | SAS model
Table of contents
Simulation Setup / Physics / Models

## Slide 12: Material Properties
- Fluid | 
- water-liquid | 
Density | 998.2 kg/m^3
Viscosity | 0.001003 kg/(m s)
- air | 
Density | 1.225 kg/m^3
Viscosity | 1.7894e-05 kg/(m s)
- Solid | 
- aluminum | 
Density | 2719 kg/m^3
Table of contents
Simulation Setup / Physics / Material Properties

## Slide 13: Cell Zone Conditions
- Fluid | 
- fluid | 
Material Name | water liquid
Specify source terms? | no
Specify fixed values? | no
Frame Motion? | no
Mesh Motion? | yes
Relative To Cell Zone | -1
Moving Mesh Rotation Speed [rad/s] | 0
Moving Mesh X-Velocity Of Zone [m/s] | 0
Moving Mesh Y-Velocity Of Zone [m/s] | 0
Moving Mesh User Defined Zone Motion Function | none
Laminar zone? | no
Table of contents
Simulation Setup / Physics / Cell Zone Conditions (1 of 2)

## Slide 14: Cell Zone Conditions
Porous zone? | no
- Solid | 
- solid | 
Material Name | aluminum
Frame Motion? | no
Mesh Motion? | no
Solid Motion? | yes
Relative To Cell Zone | -1
Solid Body Rotation Speed [rad/s] | 0
Solid Motion X-Velocity Of Zone [m/s] | 0
Solid Motion Y-Velocity Of Zone [m/s] | 0
Solid Motion User Defined Solid Motion Function | none
Table of contents
Simulation Setup / Physics / Cell Zone Conditions (2 of 2)

## Slide 15: Boundary Conditions
- Wall | 
solid_walls-shadow | wall
- solid_walls | 
Wall Motion | Stationary Wall
Shear Boundary Condition | No Slip
Wall Roughness Height [m] | 0
Wall Roughness Constant | 0.5
- outer_walls | 
Wall Motion | Stationary Wall
Shear Boundary Condition | No Slip
Wall Roughness Height [m] | 0
Wall Roughness Constant | 0.5
Table of contents
Simulation Setup / Physics / Boundary Conditions

## Slide 16: Reference Values
Area | 1 m^2
Density | 1.225 kg/m^3
Depth | 1 m
Enthalpy | 0 J/kg
Length | 1 m
Pressure | 0 Pa
Temperature | 288.16 K
Velocity | 1 m/s
Viscosity | 1.7894e-05 kg/(m s)
Ratio of Specific Heats | 1.4
Yplus for Heat Tran. Coef. | 300
Reference Zone | fluid
Table of contents
Simulation Setup / Physics / Reference Values

## Slide 17: Solver Settings
- Equations | 
Flow | True
Turbulence | True
- Numerics | 
Absolute Velocity Formulation | True
- Unsteady Calculation Parameters | 
Number of Time Steps | 100
Time Step Size [s] | 0.5
Max Iterations/Time Step | 40
- Under-Relaxation Factors | 
Pressure | 0.3
Density | 1
Body Forces | 1
Table of contents
Simulation Setup / Solver Settings (1 of 3)

## Slide 18: Solver Settings
Momentum | 0.7
Turbulent Kinetic Energy | 0.8
Specific Dissipation Rate | 0.8
Turbulent Viscosity | 1
- Pressure-Velocity Coupling | 
Type | SIMPLE
- Discretization Scheme | 
Pressure | Second Order
Momentum | Bounded Central Differencing
Turbulent Kinetic Energy | Second Order Upwind
Specific Dissipation Rate | Second Order Upwind
- Solution Limits | 
Minimum Absolute Pressure [Pa] | 1
Table of contents
Simulation Setup / Solver Settings (2 of 3)

## Slide 19: Solver Settings
Maximum Absolute Pressure [Pa] | 5e+10
Minimum Static Temperature [K] | 1
Maximum Static Temperature [K] | 5000
Minimum Turb. Kinetic Energy [m^2/s^2] | 1e-14
Minimum Turb. Kinetic Energy [m^2/s^2] | 1e-07
Minimum Spec. Dissipation Rate [s^-1] | 1e-12
Minimum Spec. Dissipation Rate [s^-1] | 1e-20
Maximum Turb. Viscosity Ratio | 100000
Table of contents
Simulation Setup / Solver Settings (3 of 3)

## Slide 20: Run Information
Number of Machines | 1
Number of Cores | 2
Case Read | 7.157 seconds
Iteration | 39.247 seconds
AMG | 8.20299 seconds
Virtual Current Memory | 1.09753 GB
Virtual Peak Memory | 1.21539 GB
Memory Per M Cell | 77.0347
Table of contents
Run Information

## Slide 21: Solution Status Flow Time: 50, Time Step: 100
 | Value | Absolute Criteria | Convergence Status
continuity | 0.02651931 | 0.001 | Not Converged
x-velocity | 0.0002259744 | 0.001 | Converged
y-velocity | 0.0002154885 | 0.001 | Converged
k | 3.634933e-05 | 0.001 | Converged
omega | 0.0001857765 | 0.001 | Converged
Table of contents
Solution Status

## Slide 22: Report Definitions
delta-time | 0.5 | s
iters-per-timestep | 40 | 
flow-time | 50 | s
Table of contents
Report Definitions

## Slide 23
Table of contents
Plots
Plots

## Slide 24: Residuals
Chart: Residuals
Table of contents
Plots / Residuals

## Slide 25
Table of contents
Contours
Contours

## Slide 26: contour-1
Table of contents
Contours / contour-1

## Slide 27
Table of contents
Vectors
Vectors

## Slide 28: vector-1
Table of contents
Vectors / vector-1

## Slide 29
Table of contents
Pathlines
Pathlines

## Slide 30: pathlines-41
Table of contents
Pathlines / pathlines-41